## Slide 1: Midterm Demo present
Group: I Believe I Can Fly

## Slide 2: Former Ideas
Hacking
  Hacking existing drone
    Structures
    Hardware
    Communications protocols
    Data transactions
Assumption:
  Drone is well-established
  Easy to interpret hardware
    Blocking design
Pros & Cons
  Pros: Less workload
  Cons: Highly dependent on Drone
Self-developing
  Design all parts of the drone by ourselves
    Protocols
    Circuits
    Structures
    Functionalities
Assumptions
  Materials allowed
  Familiar with the structure and operations of drone
Pros & Cons
  Pros: More design freedom
  Cons: extremely high workload

## Slide 3: Drone Test
Facts
  Time limited: Received all materials on Dec 1st (Yesterday)
  Overestimated drone performance
  sketchy drone PCB design

## Slide 4: New Ideas
Self-designed drone with hacking
  Hacking
    Borrow the shell of bought drone
    Hacking the structure
    Hacking the signals to control the servo
  Designing
    Drone side RP2040 + ESP8266
      Rp2040 for sending signals for servo control
      ESP8266 for data transaction between PC/controller and Drone
      Instruction Data will be translated to servo rotation speed and then send to RP2040
    Controller side RP2040 + ESP8266 + Pico4ML
      Using a self-designed balanced board with RP2040 for catching user movements
      ESP8266 sends data to the drone
      Pico4ML for further use

## Slide 5: Midterm Demo
Complete the whole circuit design:
Do and combine software design
  PIO in RP2040:
    UART for data transactions between RP2040 and any ESP8266
    I2C logical analyzer for data transaction between gyroscope and other device
    PWM for servo control
    Balance board part: track data from the gyroscope
Flyable
  Servos lift the drone with enough and variable rotation speed

## Slide 6: Questions
Materials
- Limited motor power for drones
- Limited space to place our own balanced board.
Hardware
  # of pins is limited, but more components
Software
- ESP8266 communication with RP2040
- How to handle the delay of motor communication to make drone fly.

## Slide 7: Questions
In order to avoid crazy spin of the aircraft, the four propellers of the quadcopter, the two adjacent propellers rotate in opposite directions
the counterclockwise reaction force (anti-torque) generated by F2 and F4 and the clockwise reaction force (anti-torque) generated by F1 and F3 cancel out, and the drone body can remain stable